QUESTION SCGC-TCAP-PSEP-19.1:

- Please provide a working electronic copy of every Excel spreadsheet (or other Excel model) that was used in preparing the updated TCAP testimony that was served on June 1, 2012.  As used throughout this data request, working Excel spreadsheets contain all data used and all formulas employed to derive the tables and charts shown in the testimony or otherwise support figures stated or conclusions drawn in the testimony.  Working Excel spreadsheets contain all links to other Excel spreadsheets in active format.

RESPONSE SCGC-TCAP-PSEP-19.1:

19.1 	SoCalGas provided the electronic copies of the excel spreadsheets used in preparing the June 1 updated TCAP Testimony to SCGC on June 18 via email.

QUESTION SCGC-TCAP-PSEP-19.2:

- Witness Schneider proposes (at 54) non-destructive examination (“NDE”) of short segments as an alternative to replacement and abandonment of “short sections.”

  - Do SoCalGas/SDG&E propose NDE for segments 1,000 feet or less?

  - Would NDE expense be treated as an O&M expense?

RESPONSE SCGC-TCAP-PSEP-19.2:

  - Yes.  Please refer to Response DRA-PZS-07-03.

  - Please refer to Response DRA-PZS-07-03.

QUESTION SCGC-TCAP-PSEP-19.3:

- Please provide the timeline as discussed at the May 30, 2012 workshop for developing criteria for determining whether it is necessary to replace rather than pressure test a pipeline.

  - Please explain how SoCalGas/SDG&E will make the criteria available to the parties to A.11-11-002.

  - Please explain how SoCalGas/SDG&E propose to make the criteria part of the record in this proceeding.

  - Please explain whether SoCalGas/SDG&E plan to obtain Commission approval of the criteria.

  - Please explain how the criteria will be applied on a case-by-case basis to determine whether it is necessary to replace rather than pressure test a pipeline.

  - Please explain whether SoCalGas/SDG&E plan to obtain Commission approval of a decision to replace rather than pressure test a pipeline.

RESPONSE SCGC-TCAP-PSEP-19.3: (Provided to SCGC on 6/11/12)

19.3.	The criteria alluded to at the May 30, 2012 workshop for determining whether a pipeline should be replaced or whether it can be taken out of service for pressure testing with manageable customer impacts is currently in the process of being developed.  SoCalGas/SDG&E anticipate that the criteria will be included in rebuttal testimony.

19.3.1	SoCalGas/SDG&E anticipate making the criteria available to parties by including it in rebuttal testimony.

19.3.2	See Response 19.3.1.

19.3.3	SoCalGas/SDG&E plan to obtain Commission approval of the general criteria for determining whether a pipeline can be pressure tested with manageable customer impacts.

19.3.4	Although the criteria is still under development, we anticipate that each pipeline will be evaluated per the criteria to determine whether it should be tested or replaced based on a determination of manageable customer impacts.

19.3.5	See response 19.3.3.

QUESTION SCGC-TCAP-PSEP-19.4:

- In the SoCalGas/SDG&E April 15, 2011 Report (at 5), SoCalGas/SDG&E said that Category 3 includes pipelines that “have a documented highest historical operating pressure that is at least 1.25 times the current MAOP” and that Categories 1, 2, and 3 pipelines “do not require further action.”  At the top of page 6 of the April 15, 2011 Report, SoCalGas/SDG&E say that “the reduction of the MAOP of Line 1600 to a level that results in a 1.25 times safety margin…will meet the criteria for placement in Category 3.”  At page 10, SoCalGas says that the “reductions in pressure will virtually eliminate all Category 4 Criteria Miles for SDG&E.”  However, in their 8/26/11 testimony SoCalGas/SDG&E place Line 1600 in Category 4.

  - Why did SoCalGas/SDG&E change the definition of Category 3 pipelines between the April 15, 2011 report and the August 26, 2011 testimony?

  - Did SoCalGas/SDG&E’s decision to make this change come as a result of conferring with the CPUC staff?

  - If the answer to the previous question is “yes,” please identify the staff members with whom SoCalGas/SDG&E consulted and provide a copy of any written exchanges with said staff members that address categorization of Line 1600.

RESPONSE SCGC-TCAP-PSEP-19.4:

    - SoCalGas/SDG&E did not change the definition of Category 3 pipelines.  Please refer to Response SCGC-TCAP-PSEP-17.6.4 for a description of the outcome related to the pressure reduction on Line 1600 referenced above.

    - N/A

    - N/A

QUESTION SCGC-TCAP-PSEP-19.5:

- Witness Schneider now proposes says (at 59): “This in-service natural gas pressure test is functionally equivalent to a strength test of the pipeline to 1.39 times the reduced MAOP.”

  - Please explain the rational for using the 1.39 factor rather than the 1.25 factor that SoCalGas/SDG&E proposed to apply in moving Line 1600 into Category 3 in the SoCalGas/SDG&E April 15, 2011 Report.

  - Did SoCalGas/SDG&E in-service testing and the development of the appropriate safety factor with CPUC staff members or staff members of any other state or federal agency?

  - If the answer to the previous question is “yes,” please identify the agency and staff members with whom SoCalGas/SDG&E consulted and provide a copy of any written exchanges with said staff members that address in-service testing and the development of the appropriate safety factor.

RESPONSE SCGC-TCAP-PSEP-19.5:

  - Please refer to Response DAO-20-6a.

  - No.

  - N/A

QUESTION SCGC-TCAP-PSEP-19.6:

- Please describe the adverse effects taking SDG&E Line 1600 out of service for pressure testing would have.

  - If Line 1600 were pressure tested, could deliveries through Otay Mesa be used to minimize adverse effects on service to customers.

RESPONSE SCGC-TCAP-PSEP-19.6:

19.6	If Line 1600 is removed from service for pressure testing without a replacement pipeline in place, the SDG&E system capacity will be reduced by approximately 100 MMcfd to 490 MMcfd summer/530 MMcfd winter.  This level of capacity is insufficient to meet the forecast 1-in-10 year cold day planning standard mandated by the CPUC (refer to attached San Diego Gas & Electric Company Gas Capacity Planning and Demand Forecast Semi-Annual Report, April 2012) or a high electric generation demand day in the summer operating season.

 

Additionally, an inspection may discover anomalies that may require an outage for certain segments of Line 1600.  Should this happen, customers that were served from those segments, including core customers served by distributions systems supplied by those segments, will be offline until alternate service can be provided from another pipeline or unimpacted segment of Line 1600.  This could involve the installation of several miles of temporary pipeline, which will delay restoration of service.

19.6.1	Supply delivered at Otay Mesa will mitigate the capacity impact resulting from removing Line 1600 from service for pressure testing for SDG&E customers, but, gas coming from Otay Mesa could not be utilized by the customers served off of Line 1600 in the situation described above.  Further, supply at Otay Mesa may not always be available in sufficient quantity to fully mitigate a Line 1600 capacity loss, nor is gas regularly delivered to this receipt point.